## Slide 1
Strategic Evaluation of Generation Options for SMU/NAPE
Assessing Build, Buy, and Co-Location Models for Long-Term Reliability & Growth
Team Members: Anh Bui, Minh Nguyen, Cuong Nguyen

## Slide 2
Intro to Business
Business Overview
• Power generation developer/operator
• Clients: Hyperscalers (AI, cloud), data centers
• 13,000 MW owned capacity (coal, gas, nuclear)
• Operating in PJM RTO
• Market Cap: $20B | EV: $23B | EV/EBITDA: 30x
• Adj FCF/Share: $10.20 | Target: 30%+ growth
Current Situation & Challenges
• Demand outpacing grid growth
• Policy & decarbonization pressure
• Capital & execution constraints
• 8% cost of debt, 12% cost of equity
• 60/40 debt-equity structure
• BB credit rating limits flexibility
Existing Generation Fleet
Nuclear Baseload: 2,200 MW | Gas Peaker: 3,100 MW | Gas Baseload: 3,400 MW
Coal Intermediate: 600 MW | Coal Baseload: 200 MW | Coal/Gas Intermediate: 1,400 MW

## Slide 3
Build
In consideration of Market Competition & Financial Situation
550 MW CCGT — Case Excel Assumptions
• CF ~60% → ~2.89 TWh/yr (capacity × CF × 8,760)
• Gas = 40–45% of U.S. generation; backbone dispatchable fuel
Capex & Returns
• Capex = $1,150/kW → ~$633M
• Merchant PJM pricing volatile; capacity auctions uncertain
• Returns depend on securing long-term contracts
Competitive Positioning
• Meets dispatchable needs, but weaker ESG vs nuclear/renewables
• AI firms increasingly pursuing low-carbon power partnerships
Industry Context
• Tariffs & supply-chain issues make renewables pricier
• Higher interest rates increase cost of capital
• ~12.3 GW of U.S. capacity retiring in 2025 (mostly coal/gas)

## Slide 4
Buy
In consideration of Market Competition & Financial Situation
Immediate Capacity & Cash Flow
• Acquire existing 550 MW CCGT (~$450M modeled)
• CF ~70% → ~3.37 TWh/yr, no construction delay
Asset & Carbon Risk
• Older units → efficiency decay; higher O&M
• Gas = ~875 lb/MWh CO₂ → policy exposure
• LNG export growth → greater gas price volatility
Strategic Fit
• Fastest capacity addition but non-scalable
• Nuclear (18–20% of U.S. supply) grows mainly through life extensions, limiting acquisition supply
• Regulatory risk: future EPA rules require older thermal units to retire or install 90% carbon capture
• Buy gives fast megawatts but locks into carbon-exposed, aging assets that don't scale well

## Slide 5
Partner
In consideration of Market Competition & Financial Situation
Economic Strength
• Long-term offtake → stable cash flow
• Shared capex improves IRR vs pure Build
• Avoids full merchant PJM exposure
Market Alignment
• Data centers: 415 TWh/yr globally; U.S. = 45%
• Nearly half of U.S. capacity in 5 clusters
• PJM/NoVA = epicenter
• AI firms already partnering to reopen nuclear
Competitive Advantage
• Co-located supply aligns reliability + sustainability
• Most repeatable model across DC hubs
Key Takeaway
• Matches customer demand, stabilizes revenue, reduces PJM volatility exposure
• Partner is the strongest option from a competitive standpoint

## Slide 6
Build
In consideration of Operational & Execution (Resources & Supply Chain)
Execution Burden
• Industry-based build time: 24–30 months for CCGT
• Permitting/supply-chain delays can extend to 22–36 months
Cost Exposure
• High upfront capex; interest carry throughout construction
• Full merchant risk until COD (Commercial Operating Date)
Operational Profile
• Mid-merit plant (~60% CF in Excel)
• Higher long-term carbon cost risk vs zero-carbon tech
• Build delivers a modern unit, but only for a business with strong balance sheet and high risk tolerance

## Slide 7
Buy
In consideration of Operational & Execution (Resources & Supply Chain)
Asset Quality Uncertainty
• Existing fleet shows mixed-age coal/gas/nuclear assets
• Older assets → higher forced outages + R&M capex
Market Scarcity
• Nuclear = 18–20% of U.S. generation; growth via life extensions only
• Efficient CCGTs near load hubs competitively priced
• Limited availability of high-quality assets
Operational Downside
• No design/siting control
• Full carbon exposure retained
• Long-term operational profile is largely locked in on day one

## Slide 8
Partner (Co-location)
In consideration of Operational & Execution (Resources & Supply Chain)
Co-located Asset Profile
• 100–200 MW blocks sized to DC load (model-driven design)
• Behind-the-meter reduces interconnection delays
• Case allows behind/in-front of meter
Execution & Operations Advantages
• Long-term contracts → predictable dispatch
• Smaller modular builds lower EPC exposure
• AI firms already structuring JVs with power producers
Complexity
• JV structure, shared capex, regulatory load
• Higher upfront coordination, lower long-term risk
• Revenue and offtake are contracted — operational risk is lower

## Slide 9
How Partner Can Look Like?
Goal
• 100–200 MW blocks sized to DC load
• Behind-the-meter reduces interconnection delays
• Case allows behind/in-front of meter
What SMU/NAPE Brings
• Expertise operating gas, solar, and nuclear assets
• Deliver firm dispatchable capacity, zero-carbon baseload
• 13,000 MW fleet across PJM including Northern Virginia
Illustrative Co-location Structure
• 150 MW CCGT + 50 MW Solar serving a single AI campus
• 15–20 year PPA with fixed or indexed pricing
• Cost-plus or regulated-like return structure
• Hyperscaler co-funds capex; SMU/NAPE owns & operates
Vertical Suggestions
• AI & hyperscale campuses — large loads, ~12% growth/yr
• Enterprise & government HPC — reliability-sensitive
• Renewable-mandated hubs — states requiring low-carbon
• Partner model scales well and repeats easily

## Slide 10
Our Forecast and Estimation
1. Annual Energy Generation
• Scenario A (Nuclear): 6.45 TWh/year (92% CF)
• Scenario B (Build Gas): 3.37 TWh/year (70% CF)
• Scenario C (Acquire Gas): 2.89 TWh/year (60% CF)
Nuclear provides 2.23x more annual energy than
existing gas acquisition, matching world-class uptime.
3. Total Capital Investment
• Scenario A (Nuclear): $3,000M ($3,750/kW)
• Scenario B (Build Gas): $687.5M ($1,250/kW)
• Scenario C (Acquire Gas): $450.0M ($818/kW)
Nuclear requires 4.4x more capital but delivers
zero-carbon baseload without construction delay.
Key Takeaway
Even with the least capital investment among all options, co-located Partner still generates the highest return
on energy output — making it the most capital-efficient strategy by far.

## Slide 11
Our Forecast and Estimation
4. Net Present Value (NPV) at 7.68% WACC
• Scenario C (Acquire Gas): +$63.7M (Positive DCF)
• Scenario B (Build Gas): -$133.6M (Value destructive)
• Scenario A (Nuclear): -$1,466.8M (Base case @ $60 PPA)
STRATEGIC UPSIDE: Nuclear NPV becomes positive
at $68/MWh; Meta deal was $85-90; Microsoft was $100.
4. LCOE Component Breakdown
• Nuclear: $65.41/MWh (Capital heavy, zero carbon)
• Build Gas: $55.65/MWh (Fuel-driven, carbon exposed)
• Buy Gas: $53.86/MWh (Best merchant margin)
At $100/ton carbon: Gas costs rise by $36/MWh,
swinging advantage permanently to Nuclear.
Key Insight
Co-Located Nuclear dominates — it's the only option creating substantial shareholder value.
Build CCGT barely breaks even. Acquiring nuclear outright destroys value due to excessive purchase price.

## Slide 12
Our Forecast and Estimation
6. Free Cash Flow & Investor Benefit
• Hybrid Strategy (Partner+Buy) Adj FCF/Share: $13.80 (diluted) vs $10.20 base
• FCF/Share Growth: 35.3% (vs 30% target) — Exceeds Management Goal
• Market Multiple: 30x → 35-40x re-rating driven by 'AI infrastructure' story
• Market Cap Potential: $20B → $44B+ (+122% value creation)
• Credit Upgrade: BB to BBB potential adds $565M in debt savings (NPV)
Cash Flow Stability Comparison
Partner delivers the most stable and sustainable free cash flows over the entire projection period.
This stability is critical for meeting the company's 30%+ Adj FCF/Share growth target.

## Slide 13
Our Forecast and Estimation
8. Net Profit After Tax and Depreciation — Annual Net Income Trajectory
For steady-state annual net income (Years 7–17):
• Co-Located Nuclear: ~$225M/year — Stable, contracted baseload economics
• Buy Existing Gas: ~$70M/year — Limited by merchant risk and carbon pressure
• Build New CCGT: ~$70M/year — Faces identical market constraints
Strategy Wins: Nuclear delivers 3.2x higher annual earnings than gas alternatives.
Key Insight
The nuclear co-location partner option delivers 3.2x higher annual earnings than gas alternatives,
driven by contracted revenues with data center partner eliminating merchant exposure.

## Slide 14
Risk Assessment & Solution
Risk 1: Dependence on single data center partner
The risk of relying on a single hyperscaler gives
them too much control over pricing and revenue stability.
Solutions:
• Diversify partners and global locations
• Use strong SLAs with clear performance & exit terms
• Expand into regions like Vietnam, India, Philippines
Risk 2: Complex revenue sharing
Unclear or complicated revenue-splits can lead
to disputes and hurt margins.
Solutions:
• Standardize contracts into simple pricing tiers
• Implement automated revenue-management tools
to apply formulas consistently
Summary
Both risks are manageable through diversification, standardized contracts,
and automated revenue management tools.

## Slide 15
Risk Assessment & Solution
Risk 3: Operational misalignment
Engineering, finance, and commercial teams move
at different speeds, which can slow down execution
with the data-center partner.
Solutions:
• Align teams through shared OKRs
• Run recurring cross-functional leadership meetings
to remove blockers early
Industry Facts — The Game Changers
• PJM Queue: 170,000 MW backlog; Build = 3-4 yr wait; Partner = Bypass
• DC Load: Dominion Zone hit 20 GW by 2037 (3.5x forecast increase)
• Nuclear CF: 90.96% fleet median; perfectly matches DC uptime
• PPA Pricing: Market at $85-100/MWh vs our conservative $60/MWh
• Capacity Market: Hit record $329/MW-day; adds $96M/yr to Nuclear
Thank you for your attention!